## Slide 1: Crack Behavior of High Plastic Soil
A Comparative Study with and without Biopolymer Reinforcement
Submitted by: Akshat Aren(210104012)
Under the Supervision of: Prof. T.V. Bharat
Department of Civil Engineering, IIT Guwahati
November 2024

## Slide 2: Objective
The experiment aims to evaluate the effectiveness of biopolymers (xanthan gum and guar gum) in reducing desiccation cracking in high-plastic soils. Specifically, it seeks to:
Investigate the mechanisms of cracking in untreated high-plastic soils.
Assess the impact of biopolymers on crack reduction, soil strength, and permeability improvement.

## Slide 3: Introduction
Characteristics of High-Plastic Soils:
Rich in clay minerals like montmorillonite, with high shrink-swell potential.
Impact of Moisture Changes:
Drying causes shrinkage and cracks, reducing shear strength and increasing permeability.
Wet periods lead to swelling, structural instability, and higher maintenance costs.
Cracking in Untreated Soils:
Uneven moisture, temperature variations, and particle arrangement cause cracks up to 2.6 mm wide, impacting load-bearing capacity.
Limitations of Traditional Stabilizers:
Lime and cement stabilizers have environmental drawbacks, such as high carbon emissions.
Emergence of Biopolymers:
Eco-friendly xanthan gum and guar gum reduce cracks by forming hydrogels, cutting crack width by 65% and density by 46%.
Scope of the Study:
Explore crack formation mechanisms, biopolymer treatment impact, and methodologies for analyzing soil behavior.

## Slide 5: Literature Review
Cracking in High-Plastic Soils: High-plastic soils, rich in minerals like montmorillonite and illite, experience shrinkage-induced cracks during drying and swelling-induced stresses during wetting. These phenomena lead to structural damage, instability, and challenges in geotechnical engineering.
1. Mechanisms of Cracking:
Shrinkage Behavior:
  Moisture loss creates tensile stresses, causing cracks.
  Dispersed particle structures and swelling minerals exacerbate shrinkage.
Geotechnical Challenges:
  Increased permeability destabilizes structures.
  Reduced shear strength compromises load-bearing capacity.

## Slide 6: Literature Review
2. Mitigation Using Biopolymers: Biopolymers like xanthan gum and guar gum form hydrogels, enhancing cohesion and reducing shrinkage.
Benefits:
  Crack density reduced by 46%, width by 65%.
  UCS(Unconfined Compressive Strength) improvement up to 630%.
  Lower permeability and better moisture retention.
3. Experimental Studies:
Laboratory Findings:
  Untreated soils exhibit large cracks (>2.6 mm).
  Biopolymers consistently reduce crack widths and improve soil strength.
Case Studies:
  Roads and landfill liners in India and Indonesia show improved stability with biopolymers.

## Slide 7: Literature Review
4. Analytical Approaches:
Simulations: ABAQUS models crack propagation and optimizes biopolymer dosages.
Microstructural Analysis: SEM and XRD reveal hydrogel networks and improved cohesion.
5. Comparison of Soils:
Untreated Soil: Crack width >2.6 mm, high permeability, and low strength.
Biopolymer-Treated Soil: Crack width ~0.9 mm, strength improved by up to 630%.
6. Limitations and Gaps:
Biodegradation reduces long-term performance.
Lack of standardization and large-scale trials limits adoption.

## Slide 8: Literature Review
7. Future Directions:
Develop durable biopolymers.
Conduct large-scale trials in diverse conditions.
Standardize protocols for soil stabilization.

## Slide 10: Methodology
1. Materials and Sample Preparation
Soil Selection:
  High-plastic expansive soils from regions like Gujarat, Andhra Pradesh (India), and Regina (Canada).
  Characterized using Atterberg limits, grain size, free swell index, and XRD analysis for clay minerals.
Biopolymer Selection:
  Xanthan gum and guar gum were chosen for their hydrophilic and gel-forming properties.
  Concentrations used: 0.5%, 1.5%, and 2% by dry soil weight.
Sample Preparation:
  Untreated Samples: Oven-dried, sieved, and compacted soils.
  Treated Samples: Biopolymers mixed uniformly with soils and aged for up to 60 days for hydrogel formation.

## Slide 11
2. Experimental Program
Crack Formation Analysis:
  Shrinkage tests under ambient and accelerated drying.
  Crack width and density measured using ImageJ software.
  Thermal imaging to analyze moisture distribution.
Mechanical and Hydraulic Properties:
  UCS Tests: Evaluated strength improvement with biopolymer stabilization.
  Hydraulic Conductivity: Assessed permeability changes via falling head tests.
  SEM Analysis: Observed micro-cracks and hydrogel networks.
Field Trials:
  Conducted on roads in Indonesia and soils in Karnataka, India.
  Metrics: Crack density reduction and UCS improvement.

## Slide 12
. 3. Cracks in Untreated High-Plastic Soils
Moisture Loss: Causes shrinkage and tensile stress, leading to cracking.
Thermal Variations: Fluctuations accelerate drying and widen cracks.
Particle Arrangement: Dispersed particles exacerbate cracking.
Impact of Cracks: Increased permeability and reduced shear strength.
4. How Biopolymers Mitigate Cracking
Hydrogel Formation: Binds particles, reduces voids, and minimizes shrinkage.
Cohesion and Strength: Enhances tensile strength and UCS by up to 630%.
Water Retention: Slows drying, maintaining moisture and mitigating cracks.
Environmental Resistance: Reduces crack widths even under cyclic conditions.

## Slide 13
5. Visualization and Analysis
Image Analysis: Crack density and width significantly reduced post-treatment.
SEM Micrographs: Show hydrogel networks sealing voids and bridging particles.
Thermal Imaging: Uniform moisture distribution in treated soils.
Simulations: ABAQUS models show reduced crack propagation with biopolymer treatment.

## Slide 14: Methodology Experiment Setup
Materials: Expansive clay and black cotton soil were treated with xanthan gum at varying concentrations.
Sample Preparation: Biopolymers (xanthan gum) were mixed with the soil, and control (untreated) samples were prepared for comparison.
Environmental Simulations: The samples underwent controlled rainfall, drying cycles, and temperature conditions to replicate real-world environmental scenarios.

## Slide 15
Testing Parameters:
Water Retention: Measured over time to assess moisture-holding capacity of the soils.
Crack Resistance: Monitored for crack formation using image analysis techniques.
Shear Strength: Tested to evaluate the mechanical stability of the treated and untreated soils.
Vegetation Growth: Germination rates, plant growth, and drought resistance were tracked to assess the impact on vegetation.
Data Analysis: Statistical tools were used to compare the performance of treated vs. untreated samples.

## Slide 19: Conclusion
Biopolymers like xanthan gum effectively reduce desiccation cracking in high-plastic soils, such as black cotton soil. Key findings include:
Crack Reduction: Crack width reduced to 0.9 mm, with a 46% reduction in crack density.
Strength Improvement: Unconfined compressive strength (UCS) increased by 630%, enhancing soil stability.
Hydraulic Benefits: Lower permeability reduces water infiltration and swelling risks.
Sustainability: Biopolymers offer an eco-friendly alternative to traditional stabilizers like lime and cement.
Overall, biopolymers provide a sustainable and effective solution for improving the stability of high-plastic soils in geotechnical applications.

## Slide 20: References
1. Smith & Jones (2018): Expansive soil behavior.
2. Gupta & Sharma (2021): Desiccation cracking analysis.
3. Indian Road Congress (2018): Guidelines on expansive soils.
4. Geological Survey of India (2020): Soil properties report.